## Slide 1
Chalumeau Family Capstone
- Musical instrument documentation capstone
- Build packet: chalumeau
- Generated: 2026-05-03
Slide 1

## Slide 2
Project Intent
- Design a family of chalumeaux that can be built in Tony's shop using
- lathe/CNC workflows, commercial reeds for early isolation tests, and
- optional handmade metal keywork. The family should cover a useful range
- without pretending the first-pass physics is final: all tone-hole
- coordinates are starting points that must be validated with a real reed,
- mouthpiece, bore, and player pressure.
Slide 2

## Slide 3
Physics Model
- The chalumeau is modeled as a cylindrical single-reed pipe that behaves
- like a stopped pipe in its low register.
- f = c / (4 * L_eff)
- L_eff = c / (4 * f)
- c = 13552 in/s at about 68 F
- body_length = L_eff - bell_end_correction - reed_end_correction
- bell_end_correction = 0.61 * bore_radius
Slide 3

## Slide 4
Hardware Alignment
- The hardware is intentionally small-shop manufacturable:
Slide 4

## Slide 5
How To Use This Packet
- Start with design.md for intent and assumptions.
- Use bom.csv, sourcing.csv, and cut-list.csv before buying or cutting.
- Use drawing-brief.md and CAD/CNC folders before machining.
- Print the packet for shopping, shop work, and validation.
Slide 5

## Slide 6
File Map
- design.md: Project intent, catalog metadata, assumptions, and validation plan.
- bom.csv: Starter bill of materials with part categories, quantities, drawing refs, and notes.
- sourcing.csv: Supplier/search tracker with specs, price/date fields, lead time, substitutes, and risks.
- cut-list.csv: Rough/final stock sizes, material, grain/orientation, operations, yield, and offcuts.
- drawing-brief.md: Manufacturing drawing and technical product sketch brief.
- assembly-manual.md: Shop-facing sequence, tools, fixtures, safety, tuning, finishing, and maintenance notes.
- validation.csv: Target/measured values, tolerance, environment, result, and tuning/build action log.
Slide 6

## Slide 7
Family Spec
Slide 7

## Slide 8
Build Workflow
- Design and assumptions
- Source materials and hardware
- Prepare stock, fixtures, and CNC/laser/lathe setup
- Assemble, tune, finish, and validate
Slide 8

## Slide 9
Sourcing And BOM
- BOM gives part categories and drawing references.
- Sourcing tracks search terms, supplier candidates, price/date, lead time, substitutions.
- Visual BOM brief turns the parts list into a presentation-ready image board.
Slide 9

## Slide 10
Shop Packet
- Cut list for lumber/sheet/blank planning.
- Assembly manual for away-from-keyboard work.
- Validation sheet for measured dimensions, tuning, pass/fail checks.
Slide 10

## Slide 11
Drawings, CAD, CNC
- drawing-brief.md defines required views, dimensions, datums, sketch intent.
- cad/ holds models and design tables.
- cnc/ holds CAM, toolpaths, setup sheets, dry-run notes.
- drawings/ holds PDFs, SVGs, DXFs, drawing exports.
- ![drawing](drawings/chalumeau-family-sheet.svg)
- ![drawing](drawings/chalumeau-soprano-c4-dimensioned.svg)
- ![drawing](drawings/keywork-lever-detail.svg)
Slide 11

## Slide 12
Images And Screenshots
- images/chalumeau1.jpg
- images/chalumeau5.jpg
- ![image](images/chalumeau1.jpg)
- ![image](images/chalumeau5.jpg)
Slide 12

## Slide 13
Validation Plan
- A4 = 440 Hz reference check.
- Tuning targets logged in validation.csv.
- Critical dimensions verified against design sheet and CAD.
- Photos and revision notes after each major step.
Slide 13

## Slide 14
Open Risks / Decisions
- TBDs in design sheet and BOM.
- Supplier price/availability not yet verified.
- Generated images marked as concept placeholders.
- Empirical corrections await measured prototype data.
Slide 14

## Slide 15
Next Actions
- Replace TBDs with measured/source-backed values.
- Verify live supplier price and availability before buying.
- Export final drawings and visual BOM images.
- Regenerate this deck and print packet after final edits.
Slide 15